## Slide 1: Geothermal Energy Hot Dry Rock Geothermal Potential of the Xujiaweizi Area in Songliao Basin, Northeastern China
Group 5:
Guilherme Mourão (96710)
Fábio Costa (108090)
Mayela Ledesma Ruiz (109225)
Pedro Manuel (96303)
Philina Niederkofler (109210)
Santiago Valencia (109166)

## Slide 2: Geological Setting
Geological characteristics
Mesozoic-Cenozoic sedimentary basin formed on a folding basement
Terrestrial strata: volcanic, volcaniclastig, sedimentary rocks
Basement: Middle Jurastic granites and Paelozoic strata
XJWZ area: upper depression layer and lower fault depression
Fig 2: Location of Songliao Basin and XJWZ, showing major structural zones in the basin (Guo et al.,2016)

## Slide 3: Geological Setting
-
Lower fault depression
Target reservoir for the HDR resource development
Denglouku group (K1d): 200m thick silt mudstone cap rock for deep geothermal energy
Yingchen group (K1yc): Thick acid volcanic rock layers
Fig 3: Schematic map of deep faults and stratigraphic cross sections in the Songliao Basin (Guo et al.,2016)

## Slide 4: Geothermal Field
Geothermal Temperature and Gradient
Data from oil and gas exploratory wells in Daqing Oilfield;
“Linear” correlation between temperature and depth;
Turning point in the fault-depression transition;
Geothermal gradient : 3.9 – 6.5 (ºC/100m)
Fig 4: Variation of geothermal temperature and gradient with depth (Guo et al.,2015)
(Guo et al.,2015)

## Slide 5
The average crustal thickness of XJWZ is only 29 km, which is caused by the crust extensional thinning and upper mantle uplift. As a result of the subduction of the Pacific plate under the Eurasian plate, the Songliao Basin suffered a strong tension function that enhances thermal activity.
Heat Source
Heat Source
The Songliao Basin suffered a strong tension function that enhances thermal activity.

## Slide 6: Geothermal Field
Geothermal Temperature and Gradient
Depth [m] | Temperature Range [ºC ] | Average Temperature [ºC]
1000 | 39 – 60 | 48
2000 | 75 – 140 | 96
3000 | 108 – 136 | 121
4000 | 144 – 18 | 162
Temperature distribution at different depths
(Guo et al.,2015)
(Guo et al.,2015)

## Slide 7: Geothermal Field
Rock thermal properties
11 rock samples from the XJWZ fault depression;
Thermal/Heat conductivy comparison.
Magmatic
Sedimentary
HDR resource evaluation
Magmatic Sedimentary
Volume method
Energy [J] | Depth [km]
 | 0 – 1
 | 1 – 2
 | 2 – 3
 | 3 – 4
2.73x
7.44x
1.18x
1.56x
(Guo et al.,2015)
(Guo et al.,2015)

## Slide 8: Geophysics
Moho Surface Depth: From 29 to 36 km, controlling the geothermal field of the region. The shallowest part of the Moho is near the XJWZ area, at a depth of 29-30 km.
Crustal Structure and Plate Tectonics: Strong tectonic forces due to the subduction of the Pacific plate under the Eurasian plate.
High-Conductivity Layer: Is 2-5 km thick (20 km deep), is found in the basin. Low resistivity and low density.
Magma Chamber as Heat Source: Likely a magma chamber resulting from mantle intrusion into the crust. The main heat source for the basin.
Curie Surface Depth: At 10-24 km, the shallowest region being also near the XJWZ area at 10-12 km, indicating high potential geothermal resources.
Fig 8: Representation of tectonic plate movements and consequences
Fig 7: Curie depth globally
Fig 6: Earth's core and Moho line representation

## Slide 9: Geophysics fracture testing
Key: Geophisical parameters of the region;
Where: Deepest well, YS2;
Little water: Dense lithology mall porosity, very thick rock;
Low pore width: less than 0.2 mm, rich natural cracks;
Yingchen temperature: 150℃-200℃.
(Guo et al.,2015)
(Guo et al.,2015)

## Slide 10: Reservoir Studies
Physical properties
Reservoir stimulation
Target reservoir
Volcanic reservoir in Yingcheng group has little water
Ancient sedimentary water
Rich natural fracture
In-situ stress gradient is 0.0246 MPa/m
(Guo et al.,2015)

## Slide 11: References
Guo, L., Zhang, Y., Yu, Z., Hu, Z., Chengyu, L., & Xu, T. (2015). Feasibility Evaluation of EGS Project in the Xujiaweizi Area: Potential Site in Songliao Basin, Northeastern China.Proceedings World Geothermal Congress.https://www.geothermal-energy.org/pdf/IGAstandard/WGC/2015/31028.pdf
Guo, L., Zhang, Y., Yu, Z., Hu, Z., Chengyu, L., & Xu, T. (2016). Hot dry rock geothermal potential of the Xujiaweizi area in Songliao Basin, northeastern China. Environmental Earth Sciences, 75(6). https://doi.org/10.1007/s12665-016-5327-9
Multi-stage Texas geothermal well to debut oilfield completion technologies. (n.d.). https://www.worldoil.com/magazine/2022/may-2022/special-focus-well-completion-technology/multi-stage-texas-geothermal-well-to-debut-oilfield-completion-technologies/
Zhang, L., Chen, S., & Zhang, C. (2019). Geothermal power generation in China: Status and prospects. Energy Science & Engineering, 7(5), 1428–1450. https://doi.org/10.1002/ese3.365
Zhang, Y., Li, Z., Guo, L., Gao, P., Jin, X., & Xu, T. (2014). Electricity generation from enhanced geothermal systems by oilfield produced water circulating through reservoir stimulated by staged fracturing technology for horizontal wells: A case study in Xujiaweizi area in Daqing Oilfield, China. Energy, 78, 788–805. https://doi.org/10.1016/j.energy.2014.10.073

## Slide 12: Thank you for your attention!